Here is the write up promised for using the MB blower motor in your E32 or E34.

A replacement blower motor only is sold for the Mercedes W201 chassis for around $90 at autohausaz. This motor is nearly a direct replacement, the difference being the "can" of the motor is 12mm shorter.

Remove your old blower cages by twisting them in opposite directions, one will twist off gradually by twisting back and forth. The other can be removed in the same manner but now holding the opposite bare shaft with a locking plier.

The cages will press on the shafts of the new motor with a soft mallet striking the hub area, once it's flush use a pipe over the shaft that fits on the hub.

At the top is a new BMW replacement assembly, center is the old motor, bottom is the MB motor (0 130 111 109). Note the dimensions. The shafts are also slightly shorter but still long enough.

Here is a block of wood 12mmx45mm cut from ½” stock used to fill the space.

Note the 2 tabs on the right side, these insert on the brush side of the motor.

Bare motor and block in place

On left is the assembly with the 109 motor, right is the OE replacement.

The red line indicates the plane of the inner edge of the left (driver in US) side blower cage.

The inner edge of the cage should be in alignment with the bearing holder of the motor. Once this is established, the other cage is pushed on until the overall dimension from outside to outside is 238mm.

Complete assembly installed. At this point run the motor in ALL speeds to check for interference between the cages and housing. Adjust if necessary. Install the cover, check for interference again.

I only checked with the motor on high speed, apparently the cages tend to self center at higher speed as mine made noise on low speed and needed to be readjusted.

One of the mouse condos from the evaporator compartment